## Slide 1: Diagnosing the Weakest Link in WSN Testbeds: A Reliability and Cost Analysis of the USB Backchannel
Pablo Guerrero, Iliya Gurov, Kristof Van Laerhoven, Alejandro Buchmann

## Slide 2: Testbeds 101
Debugging and reprogramming used often in experimentation
Testbed’s goal: to facilitate WSN experimentation through
  centralized node reprogramming, and
  data collection for posterior evaluation.
Expensive scientific instrument:
  initial acquisition and deployment
  maintenance and operation
this work’s topic:
“backchannel”
a) (remote) users
b) server
c) sensor network

## Slide 3: USB as Wired Interface to Sensor Nodes
USB (probably) first introduced with Telos design
  USB-to-serial chip to access MCU
  node powered via USB port, if connected

## Slide 4: Wired, USB Backchannel
server
sensor network
without support layer - 1:48 [SignetLab]
USB

## Slide 5: Wired, USB Backchannel
server
sensor network
with support layer
support layer
Ethernet
USB

## Slide 6: Wired, USB Backchannel
server
sensor network
with support layer
support layer
Ethernet
USB
- 1:{2..6} [TUDμNet, TWIST]
- 1:22 [Indriya]

## Slide 7: Challenges
Permanent, distributed sensor network testbeds require unattended operation. But:
Bug(s) in USB implementation, USB hardware, bootstrap loader, power variations, etc.  hard to reproduce!
Goals: high reproducibility, comparability, and availability of nodes
Chart: Node Reprogramming
| Jobs w/o failed nodes | Jobs with % failed nodes > 0%
Job Reprogramming | 0.1135 | 0.8865

## Slide 8: Systematic Evaluation
Methodology:
  set up backchannel [node(s), cable(s), hub(s)]
  test power and enumeration
  run micro-benchmark
    repetitively reprogramming a node (until failure / 1000 times)
Metrics:
  reprogramming time, [seconds]
  reprogramming cycles between failures, RCBF, [cycles]

## Slide 9: USB Backchannel Topologies
A Universal Serial Bus is a layered star topology:
  hubs at each star’s center
  127 devices max.
  7 layers max.
Cables
  passive: up to 5m long
  active: up to 12m long
Hubs
  passive (bus-powered)
  active (self-powered)

## Slide 10: Node Evaluation: Test Files and Reprogramming Time
FTDI chip
SiLabs chip

## Slide 11: Node Evaluation: Manufacturers
FTDI chip
SiLabs chip
reliability independent of manufacturer and USB chip

## Slide 12: Topology Evaluation: Single Node Tests, Passive Cables
Reprogramming Time per Cycle (secs)
Total USB Cable Length (m)
Reprogramming Cycles Between Failures
passive cables: up to 10 meters

## Slide 13: Topology Evaluation: Single Node Tests, Active Cables
Reprogramming Cycles Between Failures
Reprogramming Time per Cycle (secs)
Total USB Cable Length (m)
active cables: < 40 m (unreliable) or < 10m (reliable)

## Slide 14: Topology Evaluation: Single Node Tests, Active Hubs + Passive Cables
Reprogramming Cycles Between Failures
Reprogramming Time per Cycle (secs)
Total USB Cable Length (m)
active hubs and passive cables: 54m (unreliable) or 43m (reliable)

## Slide 15: Topology Evaluation: Multi Node Tests, Topologies
3x3
3x5
6x4
6x6
7x7
8x8
stable topologies: balanced trees

## Slide 16: Topology Evaluation: Multi Node Tests, Microbenchmark
Extensions:
  maximum parallelism
  node grouping
N1
N2
N3
N4
1st
N1
N2
N3
N4
time
N5
N6
N7
N8
time
2nd
3rd
4th
1st
2nd
3rd

## Slide 17: Multi Node Tests: Gateway Selection & Parallelism
 | slug | buffalo | pc
max ¦¦° | 5 | 8 | 59
Chart: 
| 4 | 12 | 24 | 48 | 64
slug | 1 | 3 | 5 | 10 | 13
buffalo | 1 | 2 | 3 | 6 | 8
pc | 1 | 1 | 1 | 1 | 2
more nodes  faster gateway needed (*)
real: 36% faster
parallelism can and should be exploited

## Slide 18: Multi Node Tests: Gateway Selection & Parallelism (2)

## Slide 19: Enhancing Backchannel Reliability
Manual node reconnection costly
Solution: resort to hub port power control
  per port power switching
  ganged power switching

## Slide 20: Enhancing Backchannel Reliability: Quantification
choose HPPC-enabled hubs

## Slide 21: Conclusions
USB is method of choice for testbed’s backchannels
Standard’s cabling restrictions can be overcome
Stable multi-node topologies can be built
HPPC-enabled USB hubs improve reliability